User Manual for model AE-F3000 continuous flow Training Smoke Machine.
Note: designed for water base fog fluid.

Menu switch:
To go back = press and hold the menu key for 1 second to return to the previous interface
UP = "+" key.
DOWN = "-" key
ENTER = confirm key
Main interface display description:
When the machine is not in operation for 60 seconds, the screen will automatically return to the main interface
The upper left corner of the screen displays the heating progress percentage. When the "98%" is displayed, it means that the heating has been completed, and when the "--%" is displayed, it means the heating error or in progress.
The upper right corner of the screen shows the temperature near the main control circuit board inside the chassis.
The second line of the screen shows the heating state.
When it is displayed as "K Error", it means thermocouple error.
When it is displayed as "Heater error" , it means there is an error of the heater.
When it is displayed as "Ready", it means heating is completed
When it is displayed as "Enter Pump", it means that the machine is under oil-free protection.
If the display board displays "Oil Free", first press ENTER until it displays "ENTER PUMP", and then long press the MENU key until it displays menu main page and press the (Detailed diagram below) ENTER key to display PUMP, then oil-free protection status is eliminated, and the oil pump begins to work.
Operation instructions of main interface:
MENU: Switch and enter the menu main interface.
UP: It is the shortcut key for continuous output.
Currently, the screen interface is in the corresponding menu page interface (when the machine is working, press ENTER to stop work before performing other operations)
DOWN: It is the shortcut key for timer output. Currently, the screen interface is in the corresponding menu page interface (when the machine is working, press ENTER to stop work before performing other operations)
ENTER: Press ENTER key to pump oil when there is no oil in the machine (Oil can be pumped only when the display interface is the main interface),
Long press ENTER key to toggle between the heating progress percentage and heater temperature display.
Precautions *
Suitable for indoor or outdoor use.
Please make sure that the power supply is the correct rated voltage before use 110V for Canada
No flammable liquids should ever be used. Water based smoke juice only.
When spraying fog, the temperature of the fog nozzle is as high as 40~100 ℃, and a safe distance of more than 100cm shall be kept from the nozzle during use.
The mist machine shall be used in a well- ventilated place, and the heat dissipation hole of the smoke machine shall not be covered to ensure proper ventilation and heat dissipation. Keep a space of at least 20cm above and below the mist machine, and no flammable substances can be stored within 30cm of the surrounding area. (Keep away from carpets, boards and flammable objects).
Attention during operation*
This mist machine can use DMX512 international signal standard line, and the connection is completed by connecting through "input" and "output" 3-pin XLP. When the control signal line is output and connected with the machine, make sure that the1ground,2(-) and 3 (+) signal lines corresponding to the 3-pin XLP seat on the machine should be within100M to prevent other electrical appliances from being disturbed due to the long signal line.
If the machine is corroded by moisture, water or fumigants, shut off the power supply immediately and contact your dealer. *The machine is equipped with a power cord, a handle, a pair of adjustment knobs, a remote-control transmitter and a manual as standard.
Ensure to pour out all the liquids before packaging and shipping.
Operating instructions*
Notes: Use this fogging machine for training only.
1. This machine is not required to be used vertically, but the built-in liquid container must be placed flat, and should not be tilted
2. Pour the high-quality fog juice into the container and tighten the bucket cover. Do not use inferior fog juice, otherwise it will accelerate the service life of the machine.
3. Insert the power cord into the fog machine panel, turn it to the right, and the display panel will turn on. At this time, it indicates that the machine is in the heating state and can be used normally.
4. When the machine starts to heat up, the liquid suction pipe of the machine must ensure that there is enough fog juice to absorb and use.
Warm tips: When adding fog juice, please take the bottle out of the machine before adding to avoid the damage to the machine accessories caused by liquid pouring into the machine
Important! If fog stops and is plugged up do not continue to heat as it will burn the element out, and this is not covered by warranty! If you are storing the unit for a prolonged period empty container and clean out the system by adding a small amount of 50/50 distilled water/vinegar solution. Let it heat up in well ventilated area and fog. Empty again and store away until needed for next training session.